- Wash hands thoroughly, do not open sample bottle until you are ready to proceed.  Sample results are dependant on proper sampling technique.

- Sample must be taken from a tap that is representative of the water distribution system, preferably from the sample tap located at or near the water pressure tank.  If the pressure tank is not accessible, the sample shall be collected from another water tap that is representative of the drinking water system.

- Water tap must be free of aerators, strainers, hose attachments, mixing type faucets, and purification devices.

4.	The COLD water tap shall be used and the service line cleared before sampling by running the water for at least two minutes, or until the temperature changes. Adjust the flow so the water runs without splashing.

5.	Do not touch the inside of the sample bottle or cap.

6.	Do not rinse sample container (white powder is a preservative).

- Sterile sample containers must be filled to at least the 100 ml line so sample volume is sufficient to perform all required tests.  Leave at least a one-inch air space to facilitate mixing of the sample by shaking.

8.	While the water is running, unscrew the cap and hold it downward.  Do not put the cap down.  Do not turn the cap upward. Fill the bottle without splashing. Screw the cap back on before turning off the water.

The sample collector is responsible for properly packaging and returning the samples to the laboratory for analysis. Chill and protect from sunlight.  All samples collected must be received by the laboratory within twenty-four hours.  Upon delivery, the sample collector will relinquish custody of the samples to laboratory personnel.

The following information must be entered on a Chain of Custody form in indelible ink:

- Name of system/owner

- WSSN/Clint ID, if applicable

- Sample number

- Sample site location (sample tap, kitchen sink, etc.)

- Sample type (routine, resample, complaint, etc.)

- Date of collection

- Time of collection

- Disinfectant residual

- Name of sampler/organization

- Transport/relinquished by information

For Repeat Collectors:

I have reviewed and fully understand the field sampling procedures outlined above. I agree to follow these procedures whenever I collect drinking water samples.

_____________________________________ ________________________

Signature Date